## Slide 1
Linear Circuit Analysis II
EECE 202 – Spring 2025
Signals

## Slide 2
Announcement
Project Proposal will be released next week
Form project groups.

## Slide 3
Recap
Syllabus introduction
Linear Circuit Analysis I revision of important concepts
New Material
Signals

## Slide 4
2. an ability to compute responses of linear circuits with and without initial conditions via one-sided Laplace transform techniques. SO [1]
Learning Outcomes

## Slide 5
Basic Signals
1- Unit step function.
2- Impulse function.
3- Ramp function.

## Slide 6
When a voltage is switched on or off in an electrical circuit at a specified value of time t.
The switching process can be described mathematically by the function called the Unit Step Function.
Unit Step Function
Notes: And Quantitative data can also be Discrete or Continuous:
Discrete data can only take certain values (like whole numbers)
Continuous data can take any value (within a range)
Put simply: Discrete data is counted, Continuous data is measured

## Slide 7
When a voltage is switched on or off in an electrical circuit at a specified value of time t.
The switching process can be described mathematically by the function called the Unit Step Function.
Unit Step Function
Unit step function: u(t) =
Unit step function: u(t) =
salman
Notes: And Quantitative data can also be Discrete or Continuous:
Discrete data can only take certain values (like whole numbers)
Continuous data can take any value (within a range)
Put simply: Discrete data is counted, Continuous data is measured

## Slide 8
Shifted Step Function
f(t)=u(t-T), time-delayed unit step signal
Often represent voltages that turn on after a prescribed time period T.
+T
Shift Right
-T
Shift Left

## Slide 9
Example
Obtain the suitable function for the following graph
f (t) = u(t-3)
Shifted step:
f(t)=u(t-T)
T=3

## Slide 10
Flipped Step Function
In flipped step function, the step takes on the value of unity for time t≤T.
f(t)=u(T-t)

## Slide 11
Represent each of the following functions as sums of step functions:
Exercise (p. 549)
f (t) = u(t)-u(t-2)
f (t) = u(-1-t)+u(t-1)
f (t) = u(t+3)-u(t-6)

## Slide 12
Ramp Function
A Ramp function models signals having a constant rate of increase
A Ramp function is the integral of the unit step function

## Slide 13
Ramp Function
A Ramp function models signals having a constant rate of increase
A Ramp function is the integral of the unit step function
r(t) = tu(t) =
salman

## Slide 14
Express the following figures in terms of steps and ramps
(a)
(b)
Example 12.2 (p. 550)

## Slide 15
f (t) = r(t)- r(t-T)
f (t) = r(t)- r(t-T)-2Tu(t-3T)
Example 12.2 (p. 550) cont.

## Slide 16
Impulse Function
The Impulse function is also named Delta Function (δ(t))
δ
The delta function has infinite height, zero width, and a well defined area of 1 unit

## Slide 17
f(t) = r(t+T)- 2r(t)+r(t-T)
Example 12.3 (p. 551)

## Slide 18
Represent f (t ) as a sum as steps, ramps, shifts of basic signals
Exercise 8 (p. 593 (a) )
f (t) =r(t)- r(t-1)+r(t-2)
f (t) =r(t)- 2 r(t-2T)+r(t-4T)

## Slide 19
Represent f (t ) as a sum as steps, ramps, shifts of basic signals
f (t) =Ku(t)- r(t-T1)+r(t-T2)
Exercise 10 (p. 594 (b) )
1
f (t) =2u(t)- r(t-T1)+r(t-T2)

## Slide 20
Additional example 1
f (t ) = 3u(t )+ u(t −1)− 2u(t − 2)− u(t − 3)− u(t − 4)
Represent f (t ) as a sum as steps, ramps, shifts of basic signals

## Slide 21
Example 2
Represent f4 (t ) as a sum as steps, ramps, shifts of basic signals
f4(t ) = 2t u(t )- 2(t −2) u(t − 2)− 2(t − 6) u(t − 6)+2(t-7)u(t-7)

## Slide 22
Practice
Use ChatGPT to answer following:
Explain the Unit Step Function and its significance in circuit analysis.
What is a flipped step function, and how is it different from the standard unit step function?
Define the ramp function and explain its relationship with the unit step function.
What is the impulse function, and how does it differ from the unit step function?

## Slide 23
Suggested Additional Problems for Ch. 12:
Exercise 8 (p. 593 (b) ), 10 (p. 594 (a) ), 7
Unit Step Function
  Describes voltage switching on/off in a circuit
  Example: f(t)=u(t−T)
Ramp Function
  Models signals with constant increase rate
  Integral of the Unit Step Function
  Impulse (Delta) Function
  Represents an instantaneous change in signal with zero width and infinite height
Shifted and Flipped Step Functions
  Shifted Step: f(t)=u(t−T)
  Flipped Step: f(t)=u(T−t)
Signal Composition
  Representing complex functions using sums of steps, ramps, and shifts
  Example: f(t)=r(t) - 2r(t-2T) + r(t-4T)f(t)=r(t)−2r(t−2T)+r(t−4T)
Summary