## Slide 1
Linear Circuit Analysis II
EECE 202 – Spring 2025
Laplace Transform Analysis

## Slide 2
Announcement
Project Proposal will be released next week
Form project groups.
Quiz during Week 4

## Slide 3
Recap
Introduction to basic signals
New Material
Laplace transform analysis
Properties of LaPlace transform
Examples

## Slide 4
2. an ability to compute responses of linear circuits with and without initial conditions via one-sided Laplace transform techniques. SO [1]
Learning Outcomes

## Slide 5
Laplace Transform Analysis
Circuit
(Differential Equation)
Input Signal
Output Signal
Laplace Transform (LT) of Circuit
(Differential Equation)
LT of Input Signal
Output Signal in Laplace domain
Laplace transform analysis technique transforms the time domain analysis of circuit, system, or differential equation to the frequency domain thus making it easier to solve.

## Slide 6
Laplace Transform Analysis
The one-side Laplace Transform of a Signal, a Function, or an Excitation is given by:
s =jω is a complex variable (a complex frequency) and j=
F(s) is the frequency domain counterpart of f(t).
Analysis using Laplase transforms is often called frequency domain analysis.

## Slide 7
U(s) = L[u(t )]=
= -
Example 12.4 (p. 556)
Find the Laplace tranform of the unit step U(s)

## Slide 8
U(s) = L[u(t )]=
= -
Example 12.4 (p. 556)
Find the Laplace tranform of the unit step U(s)
Unit Step function u(t) ={
t≥0
0 t<0
salman

## Slide 9
F(s) = L[K e-at u(t)]=
=K
Example 12.5 (p. 557)
Find F(s) for f(t)=Ke-at u(t)
Example 1
δ
Delta(s) = L[δ(t)]
Delta(s) = L[δ (t )] =
=
Find Delta (s)
Recall Delta function (or Impulse function)

## Slide 10
Properties of Laplace Transform

## Slide 11
Properties of Laplace Transform
f(t) | F(s)
δ(t) | 1
u(t) | 
r(t)=tu(t) | 
u(t) | 
Sin(ɯt)u(t) | 
cos(ɯt)u(t) | 
a(t)+b(t) | a(s)+b(s)
f(t) | F(s)
δ(t) | 1
u(t) | 
r(t)=tu(t) | 
Sin(ɯt)u(t) | 
cos(ɯt)u(t) | 
f(t) | F(s)
 | f(s+a)
f(t-T)u(t-T) | f(s)
f(t) | 
 | Sf(s) – f()
 | f(s)-sf()-f()
f(t)dt | +
f(t) | F(s)
 | f(s+a)
f(t-T)u(t-T) | 
salman

## Slide 12
The Laplace Transform operation is Linear
For f(t)= a1 f1(t )+ a2 f2 (t )
L[a1 f1(t )+ a2 f2 (t )] = a1L[f1(t )]+ a2 L[f2 (t )] = a1F1(s)+ a2 F2 (s)
Laplace transform properties and examples
Example 12.6 (p. 557)
Find F(s) when f(t)= K1 u(t)+ K2e-at u(t)
Recall LT pairs
1. Linearity property
Notes: And Quantitative data can also be Discrete or Continuous:
Discrete data can only take certain values (like whole numbers)
Continuous data can take any value (within a range)
Put simply: Discrete data is counted, Continuous data is measured

## Slide 13
Laplace transform properties and examples
L[ f (t − T )u(t − T )] = e−sT F(s)
Proof
If L[f(t )u(t )] = F(s), then, for T>0
As T is constant, then dq = dt
2. Time shift property

## Slide 14
Laplace transform properties and examples
L[ f (t − T )u(t − T )] = e−sT F(s)
Proof
If L[f(t )u(t )] = F(s), then, for T>0
As T is constant, then dq = dt
2. Time shift property
F(s)=L[f(t-T) u(t-T)} =
F(s)=
salman
=e-st f(q)e-sq dq=e-stF(s)

## Slide 15
Example 12.7 (p. 559)
Find F(s) for the signal f(t) given in the following figure
Recall LT pairs
1
2
2
1
3
-1
-2
f(t)
t
Notes: And Quantitative data can also be Discrete or Continuous:
Discrete data can only take certain values (like whole numbers)
Continuous data can take any value (within a range)
Put simply: Discrete data is counted, Continuous data is measured

## Slide 16
Example 12.7 (p. 559)
Find F(s) for the signal f(t) given in the following figure
Recall LT pairs
1
2
2
1
3
-1
-2
f(t)
t
f(t) = 3u(t) – 5u(t-1) + 2u(t-2)
F(s) =
salman
Notes: And Quantitative data can also be Discrete or Continuous:
Discrete data can only take certain values (like whole numbers)
Continuous data can take any value (within a range)
Put simply: Discrete data is counted, Continuous data is measured

## Slide 17
f (t ) = 3u(t )+ u(t −1)− 2u(t − 2)− u(t − 3)− u(t − 4)
F
Example 2
Find F(s) for the signal f(t) given in the following figure
Recall LT pairs

## Slide 18
If F(s) = L[f(t )], then L[tf(t )]=
Laplace transform properties and examples
3. Multiplication-by-t property

## Slide 19
Example 12.8 (p. 560)
Find the Laplace transform of the ramp function R(s)=L[r(t)]
Recall Ramp function

## Slide 20
Example 12.8 (p. 560)
Find the Laplace transform of the ramp function R(s)=L[r(t)]
Recall Ramp function
R(s) = L[r(t)] = tu(t)e-stdt
=
= - e-st dt = -
=
salman

## Slide 21
f
F (
Example 3
Find F(s) for the signal f(t) given in the following figures
Recall LT pairs
A)
B)

## Slide 22
f
F (
Example 3
Find F(s) for the signal f(t) given in the following figures
Recall LT pairs
A)
B)
f(t) = ku(t) - r(t – T1) +

## Slide 23
f (t) = r(t)- r(t-T)-2Tu(t-3T)
F(s) =
Example 12.10 (p. 561)
Find F(s) for the signal f(t) depicted in the
following figure

## Slide 24
Find Vout(s) for the following Circuit
I1(t)
I2(t)
Vout(t)
+
-
10Ω
Example 12.11 (p. 562)

## Slide 25
Vout(t) = 10×(I1(t)+ I2(t))
From linearity: Vout(s) = 10×(I1(s)+ I2(s))
I1(s)= = =
I2(t)=1.5u(t)-1.5u(t-1)
Vout(s) = 10×( )
Vout(s)=
Example 12.11 (p. 562) cont.
I1(t)=2u(t)-2r(t)+2r(t-1)
I2(s)= =

## Slide 26
Laplace transform properties (Table 12.2. p.584)

## Slide 27
Determine Laplace Transform for the following function:
f(t) = 12 t e-3(t-4) u(t-4)
f(t) = t×12 e-3(t-4) u(t-4) =t×f0(t)
f0(t)=12 e-3(t-4) u(t-4) , then F0(s) =
Time Shift Property
F(s)= = +
Time Multiplication Property
Example 4

## Slide 28
Determine Laplace Transform for the following function:
f(t) = 10 t3 e-2t u(t)
f(t) = t3 ×10 e-2t u(t) = t3 × f0(t)
F0(s) =
F(s) = -
Example 5

## Slide 29
What is the primary advantage of using the Laplace Transform in circuit analysis?
Explain how the Laplace Transform simplifies solving differential equations.
Explain the time shift property of the Laplace Transform.
What is the multiplication-by-time property of the Laplace Transform?
Explain how the Laplace Transform is applied to analyze circuits in the frequency domain.
Solve activity on Moodle
Practice

## Slide 30
Suggested Additional Problems for Ch. 12:
Example 12.25 (p. 585), 12.26 (p. 587) ?
Laplace Transform Basics
  Transforms time-domain signals into the frequency domain, simplifying the analysis of circuits.
  Used to solve differential equations by transforming them into algebraic equations.
Key Properties of Laplace Transform
  Linearity
  Time Shift
  Multiplication by Time
Common Examples
  Laplace Transform of Unit Step Function
  Laplace Transform of Exponential Function
  Delta Function and its Laplace
Applications in Circuit Analysis
  Conversion of time-domain circuit equations into the s-domain for easier solution.
Summary