## Slide 1
Linear Circuit Analysis II
EECE 202 – Spring 2025
Sinusoidal Steady State Analysis

## Slide 2
Announcement
GCA2 – Group Week 11 Lecture 2
PD2 (Technical Report) due Thursday Week 12

## Slide 3
Recap
Sinusoidal steady state (SSS) sources
Laplace Transform approach to SSS
Laplace Transform approach to SSS
New Material
Switching
Series combination
Parallel combination

## Slide 4
Sinusoidal Steady-State Sources
Sources in which the value of the voltage and/or current varies with time
Why Sinusoidal Sources???
Generation, Transmission, Distribution and Consumption occur under sinusoidal Steady-state behavior
Understanding the behavior of Sinusoidal circuits makes it easy to predict The behavior of circuits with non-sinusoidal ones
Steady state sinusoidal behavior often simplifies the design of electrical systems

## Slide 5
Sinusoidal waveform
Maximum Value
Time Period
Phase Angle
Angular Frequency
Source Frequency

## Slide 6
How to express a sinusoidal varying function ?
V=Vm cos (wt+φ)
V=Vm sin (wt+φ)
Cosine Function
Sine Function
V=Vm cos (wt+φ)
Maximum
Value
Angular frequency
W = 2 π F (rad/sec)
Phase angle
Source Frequency: F (Hz)
Time Period: T (sec)
T= 1/F
Sin (wt+θ)= Cos (wt+θ-900)

## Slide 7
Sine – Cosine Conversion
Sin (wt+θ)= Cos (wt+θ-900)
Sin (wt±1800)= - Sin wt
Cos (wt±1800)= - Cos wt

## Slide 8
Example-1
A Sinusoidal voltage is given by the expression V =300 Cos (120πt+300)
What is the period of the voltage in milliseconds?
What is the frequency in Hertz?
What is the magnitude of V at t =2.778 ms?
As w = 2 πF = 120 π = 2 π/T, then T = 1/60 = 16.667 ms
As F = 1/T, then F = 1/16.667 = 60 Hz
As w = 2 π/T, then W = 2×3.14/16.667 rad/sec, then at t = 2.778 ms
wt = (2×3.14/16.667) ×2.778 = 1.047 rad; or wt = 1.047 ×1800/3.14 = 600 degrees
Then V = 300 Cos (60+30)= 300 Cos 900 = Zero V

## Slide 9
A Sinusoidal current has a maximum amplitude of 20 A, the current passes through one complete cycle in 1 ms, the magnitude of the current at zero time is 10A.
What is the frequency of current in Hz?
What is the value of angular frequency?
Write an expression for i(t) using the cosine function, express φin degrees
F=1/T =1/1×10-3 =1000 Hz
w =2πF=2000 π rad/sec
i(t)=Im cos (wt+φ) = 20 cos(2000πt +φ), but as at t= 0, I=10A, then
10 = 20 cos (0+ φ)……. φ= cos-10.5 = 600, then i(t)=20 cos (2000 πt +600)
Example-2

## Slide 10
So: V(t) = Vm Cos (wt+φ)
V = Vm φ
Time domain
Phasor domain
Vm Cos (wt+φ) | 
Vm Sin (wt+φ) | 
Im Cos (wt+φ) | 
Im Sin (wt+φ) | 
V = Vm φ
V = Vm φ-900
I =Im φ
I = Im φ-900
Phasor domain representation

## Slide 11
Laplace Transform approach to SSS
K cos(ωt +θ )
Stable Circuit
with TF H(s)
s= jω
M(ω )cos(ωt +ϕ(ω ))
M(ω ) = K
ϕ(ω ) = ∠H( jω ) +θ
You just need to replace a stable H(s) by H(jw) to compute the SSS.

## Slide 12
Example -3
Suppose a second order linear circuit having the transfer function:
The transfer function is driven by a sinusoidal input . Find the steady-state response.
°

## Slide 13
Example -4
Suppose a second order linear circuit having the transfer function:
The transfer function is driven by a sinusoidal input . Find the steady-state response.

## Slide 14
Example -5
1Ω
1H
1F
Vin(t)
+
-
-
+
VOut (t)
Find Vout,ss (t) for the circuit below when vin(t) = K cos(ωt) V, K > 0. All passive RLC circuits are stable since there are no active/dependent sources.
Step 1. Find H(s)
Step 2. Find Vout,ss(s)

## Slide 15
Example -5
1Ω
1H
1F
Vin(t)
+
-
-
+
VOut (t)
Find Vout,ss (t) for the circuit below when vin(t) = K cos(ωt) V, K > 0. All passive RLC circuits are stable since there are no active/dependent sources.
Step 1. Find H(s)
Step 2. Find Vout,ss(s)
=
salman

## Slide 16
=

## Slide 17
Answer the following questions using ChatGPT
What are sinusoidal sources, and why are they commonly used in electrical systems?
How does the time period (T) relate to the frequency (f) of a sinusoidal waveform?
Why is understanding sinusoidal steady-state behavior important for analyzing circuits with non-sinusoidal inputs?
Explain the relationship between sine and cosine functions in terms of phase shifts.
Why is phasor representation particularly useful in AC circuit analysis?
How does the Laplace transform facilitate sinusoidal steady-state (SSS) analysis?

## Slide 18
Suggested examples
Page 704, example 14.8
Page 749, example 31
Page 750, example 32
Page 751, examples 36 and 37
Summary
Voltage or current varies with time following a sinusoidal function.
Sinusoidal Waveform Parameters (amplitude, frequency, angular frequency, phase)
Phasors represent sinusoidal signals as complex numbers for simplified circuit analysis.
Replacing stable H(s) with H(jω) for steady-state analysis, simplifies computation of outputs for sinusoidal inputs
Facilitates understanding of resonance and impedance in RLC circuits.