## Slide 1: Introduction
Linear Circuit Analysis
EECE 202

## Slide 2
Number of credits: 3 credits
Prerequisites: EECE 201
Contact Hours: 3 hrs Lecture
Textbook/material required: R. A. DeCarlo and P-M. Lin, “Linear Circuit Analysis; The Time Domain, Phasor and Laplace Transform Approach”, 3rd Edition, 2009.

## Slide 3
Learning Outcomes
By the end of this course, the student should be able to:
An ability to compute impedances and admittances of components and circuits. SO[1]
An ability to compute responses of linear circuits with and without initial conditions via one-sided Laplace transform techniques. SO[1]
An ability to compute responses to linear circuits using transfer function and convolution techniques. SO[1]
An ability to analyze and compute responses of linear circuits containing mutually coupled inductors and ideal transformers in the s-domain. SO[1]
An ability to analyze basic two port circuits using the various types of two port parameters and be able to construct such parameters from a given circuit. SO[1]
An ability to analyze and design basic LP, BP, HP and resonant circuits in the s-domain. SO[1]
an ability to work within a team, develop hands-on experience, draw conclusion and communicate results through the offered course project. SO[2,3,5]

## Slide 4
 | Assessment |  | Weight
Attendance |  |  | 5%
Assignments | PD1 – Conceptual Design Presentation (Week 10) |  | 3 x 10%
 | PD2 – Technical Report (10%) (Week 12) | PD2 – Prototype Demonstration | 
 | PD3 – Prototype Demonstration (10%) (Week 14) |  | 
Graded Class Activity (GCA) | GCA – 1 (Week 6, L2) |  | 2 x 10%
 | GCA – 2 (Week 11, L2) |  | 
Moodle Quiz | Quiz (Week 4) |  | 5%
Midterm | Week 8 |  | 20%
Final exam | Week 16 |  | 20%
 |  | Total | 100%

## Slide 5: Revision on EE201

## Slide 6
Resistor
Inductor
Capacitor
Passive Elements

## Slide 7
V = I×R
Ohm’s Law
Ohm’s law states that the voltage “V” across a resistor “R” is directly proportional to the current “I” flowing through the resistor

## Slide 8
As R varies from zero to infinity, it is necessary to study the relation between V and I at the extreme values of R
Short Circuit Case
R = zero, V = zero
Open Circuit Case
R = ∞, I = zero

## Slide 9
V-I characteristics according to Ohm’s law
V = I×R
I = V/R
R = V/I

## Slide 10
Power calculations according to Ohm’s Law
P = V × I
P = V2/ R
P = I2× R
V = I × R

## Slide 12
Example 7
A resistor formed of a copper conductor of length 0.1 m and cross-sectional area 4×10-4 m2, the resistivity of copper is 1.72×10-8 Ω.m find the current flowing through the resistor when a 10 V battery is connected across its terminals.
Solution
Since I = V/R
And R = δL/A = 1.72×10-8 ×0.1/4×10-4 = 43×10-7 Ω
Then I = 10/43×10-7 = 2.3 MA

## Slide 13
Nodes, Branches and Loops
Branch: represents a single element such as a voltage source or a resistor
A branch represents any element with two terminals
There are five branches in the shown figure, namely the 10 V voltage source, the 2-A current source and the three resistors.
(Vb-10)/5 - (Vb/2) - (Vb/3) – 2 = 0

## Slide 14
Node: is the point of connection between two or more branches
Nodes, Branches and Loops
A node is usually indicated by a dot in a circuit, but if a short circuit connects two nodes, the two nodes constitute a single node
There are three nodes in the shown circuit, a, b and c

## Slide 15
Loop: is a closed path formed by starting at a node, passing through a set of nodes and returning to the starting node without passing through any node more than once
Nodes, Branches and Loops
abca is a loop, where the flow from b to c could be done via: the 2 ohm resistor, the 3 ohm resistor, …………………etc

## Slide 16
Example(8)
Determine the number of branches and nodes in the shown circuit
Solution
As the circuit has four elements, then there are four branches as follows:
the 10 V voltage source
the 2A current source
the 5 ohm resistor
the 6 ohm resistor
There are three nodes in the circuit 1, 2 and 3
(V2-10/5) + (V2/6) – 2 = 0

## Slide 17
Example(9)
Determine the number of branches and nodes in the shown circuit
Solution
As the circuit has five elements, then there are five branches as follows:
the 10 V voltage source
the 1ohm resistor
the 2 ohm resistor
the 3 ohm resistor
the 4 ohm resistor
There are three nodes in the circuit 1, 2 and 3

## Slide 18
Resistor’s Arrangements
There are three possible arrangements for resistors in an electrical circuit
Series
Parallel
Series
&
Parallel

## Slide 19
Resistors in Series
V = V1 + V2 = I R1 + I R2= I (R1 + R2)
V = I Req
Two or more elements are said to be in series if they exclusively share a single node and consequently carry the same current
For N resistors placed in series
Req = R1 + R2 +……………….RN

## Slide 20
Resistors in Parallel
Two or more elements are said to be in parallel if they are connected to the same two nodes and consequently have the same voltage across them
V = I1R1 = I2R2
But since I = I1 + I2 , then
I = (V/R1 + V/R2) = V (R1+R2)/R1R2
and as, Req = V/I…then
Req = R1R2/(R1+R2)
For N resistors placed in parallel
1/Req = 1/R1 + 1/R2 +……………1/RN

## Slide 21
Conductance “G”
The conductance is a measure of how well an element will conduct electric current
The unit of conductance is “Siemens” and with the symbol of “S”
G = 1/R = I/V (S)
Note: the equivalent of N parallel resistors could be calculated using conductance, where:
Geq = G1 + G2 +…………………..GN

## Slide 22
Voltage sources placed in Series
Note the voltage source sign when obtaining their equivalence

## Slide 23
Example(10)
Solution
Find Req for the shown resistor arrangement
Req = 4 + 8 + 2.4 = 14.4 Ω

## Slide 24
Example(11)
Solution
Find Req for the shown resistor arrangement
Req = 10 + (3×2)/(3+2) = 11.2 Ω

## Slide 25
Example(12)
Solution
Find Req for the shown resistor arrangement
Try to solve
Final answer 6 Ω

## Slide 26: Inductors
31-Jan-24 Dr. Gaouda
An inductor is a two terminal passive element designed to store energy in its magnetic field.
An inductor consists of a coil of conducting wire.
Inductors store electromagnetic energy.
They may supply stored energy back to the circuit, but they cannot create energy.
They must abide by the passive sign convention
Follow passive sign
convention
L
iL (t)
+ VL (t) –

## Slide 27: Current voltage relationship of an inductor
An inductor acts like a short circuit in a DC circuit since di/dt = 0.
The inductor current cannot change abruptly.
The inductor voltage is proportional to the derivative of the current passing through it.
Where L is the inductance of the inductor and its unit is Henry (H).
L
iL (t)
+ VL (t) –

## Slide 28
Example 7.1 (page 274)
Find the voltage across the Inductor.

## Slide 29: Series and parallel inductors
The equivalent inductance of series-connected inductors is the sum of the individual inductances.
+ + … +
in:
+ + + … +

## Slide 30: Series and parallel inductors
The equivalent inductance of parallel inductors is the reciprocal of the sum of the reciprocals of the individual inductances.
(a)

## Slide 31
Capacitors
A capacitor is a passive element designed to store energy in its electric field. It consists of two conducting plates separated by an insulator (or dielectric).
Capacitance of a capacitor is the ratio of the charge on one plate to the voltage difference between the two plates, measured in farads (F).
Fixed capacitors
NOTE: 1 farad = 1 coulomb/volt.
Polyester capacitor
Ceramic capacitor
Electrolytic capacitor

## Slide 32
The current-voltage relationship of a capacitor
The charge, voltage and capacitance can be mathematically presented as:
The current in the capacitors is:
where C is the capacitance of the capacitor measured in farad (F)
NOTE
If a DC voltage is applied, the capacitor will be an open circuit.
The capacitor voltage cannot change abruptly.
Not allowable voltage change
allowable voltage change

## Slide 33
Find the voltage across a capacitor of 2 micro Farads holding 100 micro Coulomb of charge.
Determine the voltage across a 2 μF capacitor if the current passing through it is: i(t) = 6e−3000t mA. Assume v(0) =0.
Example
Example

## Slide 34
The equivalent capacitance of N parallel-connected capacitors is the sum of the individual capacitances.
Series and parallel capacitors
+
S =

## Slide 35
The equivalent capacitance of N series-connected capacitors is the inverse of the sum of the inverses of the individual capacitances.
Series and parallel capacitors
S

## Slide 36
Find the equivalent capacitance seen between terminals a and b
Example
C1
C2
C2=(20*5/25)+6=10 μF
C1=C2+10=30 μF