## Slide 1
Linear Circuit Analysis II
EECE 202
Filters – Part B

## Slide 2
Announcement
Midterm during week 8
PD 1 Voice Over PPT due in Week 10

## Slide 3
Recap
Filters
Filter Type
Transfer function of a filter
Cutoff frequency
New Material
Transfer function of LP, BP, and HP filter

## Slide 4: Low Pass Filter
The Low pass filter passes signals with frequencies below a certain value (fc), and blocks frequencies above this value. This value (fc) as shown in the figure (shows ideal filter) is called the cutoff frequency.
The characteristic shown in the figure represents the real response of the low pass filter, where the signal at the cutoff frequency (fc) is attenuated to 70.7% (-3 dB) of its original amplitude.
The frequencies below this fc is called “Pass Band”, and the frequencies above the fc is called the “Stop Band”.

## Slide 5: High pass filter
The High pass filter passes signals with frequencies above a certain value (fc), and blocks frequencies below this value. This value (fc) as shown in the figure (shows ideal filter) is called the cutoff frequency.
The characteristic shown in the figure represents the real response of the high pass filter, where the signal at the cutoff frequency (fc) is attenuated to 70.7% (-3 dB) of its original amplitude.
The frequencies above this fc is called “Pass Band”, and the frequencies below the fc is called the “Stop Band”.

## Slide 6: Bandpass Filter
The Band pass filter passes signals with frequencies between certain values (fc1, fc2), and blocks frequencies outside these values. These values (fc1, fc2) as shown in the figure (shows ideal filter) is called the cutoff frequencies.
The characteristic shown in the figure represents the real response of the band pass filter, where the signal at the cutoff frequency (fc1 and fc2) are attenuated to 70.7% (-3 dB) of its original amplitude.
The frequencies in between these fc1 and fc2 are called “Pass Band”, and the frequencies outside the fc1 and fc2 are called the “Stop Band”.

## Slide 7
High Pass Filter (HPF)
The opposite of the low-pass is the high-pass filter, which rejects signals below its cutoff frequency.
0: is the magnitude of pole frequency like in BP filter, and σ is the real part of the pole frequency
The poles of the TF are : P1,2 = -σ ± jd
The peak frequency is :

## Slide 8
The gain (amplitude) of the frequency response is given by:
The phase response is given by:

## Slide 9
1- Find the transfer function of the shown circuit.
2- What kind of filter does this circuit represent.
3-Find the peak frequency (wo) and the gain factor “K”.
Example
, and
Then the TF will be:
There is an “” on the numerator, then this is a High Pass Filter.
By matching the below 2 equations, we can easily find =1, and K =1
&

## Slide 10
Band Pass (BP) Filter
The poles of the TF are : P1,2 = -σ ± jd
The maximum value:
The general TF of a 2nd order BPF
The peak frequency is :
The Bandwidth is :
The Quality factor:

## Slide 11
Example -1
For the circuit shown, answer the following:
1-Find the transfer function H(s).
2-What kind of filter does this circuit represent.
3-Find the magnitude and the phase of the transfer function as a function of “”.
Solution
H(s) is like
so the circuit represents a
band pass filter

## Slide 12
Suppose a second-order BP-filter circuit having the transfer function:
Find Hm,, Bw and 1,2. Also, draw the response and indicate the obtained values.
p=16 rad/sec, BW=2 rad/sec, Hm=1, 1=15 rad/sec and 2=17 rad/sec.
Example -2
H(s)=
K=2,

## Slide 13
For the shown circuit, find the transfer function (s) .
Use R=2.5K Ω, L=0.1H, C=0.1uF
Also, find Hm, , Bw and 1,2.
Draw the response and indicate the obtained values.
Example -3

## Slide 14
Example -3
Compare this equation:
With the BPF equation:

## Slide 15
Example 3
Now, replace each parameter
with its value in the example.

## Slide 16
Answer the following questions using ChatGPT
How do filters affect the amplitude of signals within their pass band and stop band.
Give an example where each filter type might be practically applied in electronic or communication systems
Which property of a filter describes its ability to distinguish between closely spaced frequencies.
Which filter blocks only a specific narrow band of frequencies while passing all others.

## Slide 17
Summary
Low-Pass Filter (LPF) allows frequencies below the cutoff frequency (fc) to pass and attenuates frequencies above fc. Used to remove high-frequency noise from signals.
High-Pass Filter (HPF) allows frequencies above the cutoff frequency (fc​) to pass, attenuates frequencies below fc, useful in applications that require eliminating low-frequency noise or interference.
Band-Pass Filter (BPF) passes frequencies within a specific range (fc​1 to fc2), attenuates frequencies outside this range, and ideal for isolating specific frequency bands.
Notch (Band-Stop) Filter attenuates a narrow band of frequencies, passes frequencies outside this band, used to eliminate unwanted frequencies.
Key Concepts
At cutoff frequency signal amplitude drops to 70.7% (-3 dB).
Pass Band & Stop Band: Frequency ranges that are passed or attenuated by the filter.
Quality Factor (Q) indicates the filter's selectivity and ability to distinguish between frequencies.
.